## Slide 1
INSTRUCTION PIPELINING SIMULTION
Introduction to
Instruction pipelining simultion
Home
Content
Contact

## Slide 2
PIPELINE STAGES
The standard 5-stage pipeline includes:-
IF: Instruction Fetch
ID: Instruction Decode
EX: Execute
MEM: Memory Access
WB: Write Back
Instruction pipelining simultion
Home
Content
Contact

## Slide 3
TYPES OF HAZARDS
- RAW (Read After Write): Occurs when an instruction needs
data not yet written by a previous one.
- WAR (Write After Read): Occurs when a write overtakes a read.
- WAW (Write After Write): Occurs when two instructions write
to the same register.
Most pipeline simulations focus on RAW hazards because they
are the most common.
Instruction pipelining simultion
Home
Content
Contact

## Slide 4
SIMULATION APPROACH
Each instruction is represented with fields like operation, destination register, and source registers. A Pipeline class tracks instructions through the five stages cycle by cycle. Hazards are detected at the ID stage, and stalls are inserted if necessary. A Strategy Pattern can be used to switch between different hazard-handling methods (e.g., stall only vs. forwarding).
Instruction pipelining simultion
Home
Content
Contact

## Slide 5
EXAMPLE INSTRUCTION SEQUENCE
1. LW r1, 0(r0)
2. ADD r2, r1, r3
3. MUL r4, r2, r5
4. ADD r6, r4, r7
5. SW r6, 4(r0)
These instructions include RAW dependencies that cause stalls, especially after load instructions.
Instruction pipelining simultion
Home
Content
Contact

## Slide 6
Instruction pipelining simultion
Home
Content
Contact
Policy
Total Cycles
Stalls
IPC
Stall Only
13
3
0.38
SIMULATION RESULTS – STALL ONLY

## Slide 7
Instruction pipelining simultion
Home
Content
Contact
Policy
Total Cycles
Stalls
IPC
Forwarding
10
1
0.5
SIMULATION RESULTS – WITH FORWARDING

## Slide 8
ANALYSIS
The simulation shows that pipeline stalls occur mainly due to RAW hazards, especially load-use dependencies. Forwarding significantly reduces the number of stalls and increases IPC, but cannot eliminate all hazards. The results highlight the importance of hazard detection and data forwarding mechanisms in pipeline design
Instruction pipelining simultion
Home
Content
Contact

## Slide 9
DESIGN PATTERN IMPLEMENTATION
Instruction pipelining simultion
Home
Content
Contact
The Strategy Pattern allows flexible hazard handling strategies:
- StallStrategy: always stalls when a hazard is detected.
- ForwardingStrategy: forwards data when possible, reducing stalls.
This design makes it easy to extend the pipeline with additional strategies in the future.

## Slide 10
CONCLUSION
Instruction pipelining simultion
Home
Content
Contact
Instruction pipelining improves CPU throughput by overlapping execution stages. Hazards can reduce performance but can be mitigated through techniques such as forwarding and effective hazard detection. This simulation demonstrates how pipeline design choices affect execution time, stalls, and overall performance.